## Slide 1: SystemC Configuration Tutorial Public Review version of the draft standard
October 4, 2017

## Slide 2: Acknowledgements
This tutorial content was contributed to the Accellera SystemC CCI WG by Ericsson, GreenSocs and Doulos.

## Slide 3: Config, Control, Inspection WG
Public Review Draft
System debug
Analysis
Authoring
Checkpoint, Reverse simulation
Tool Use Cases
Parameters
Registers
Probes
Save/Restore
Commands
Configuration
State (registers, variables)
Data (performance, power,stats)
Built-in debug functionality
Standard Interfaces
Model Information
WG is defining these
Goal: Standardizing interfaces between models and tools

## Slide 4: Parameterizing a System
Peripheral subsystem IPs
CPUs
CPUs
CPUs
CPUs
System IPs - DMA, PLL, Power
Accelerator & co-processor IPs
Memory subsystem
Generally, IPs come from many vendors
On-chip bus
Parameter Examples
system clock speed
# processor cores
memory size
address, data widths
disabled IP(s)
address maps
SW image filename
IP granularity debug control*:
  logging
  tracing
Need uniform way to configure simulation without recompilation
* runtime parameters provide initial CCI “control” capability

## Slide 5: CCI Environment
CCI requires SystemC 2.3.1 and works better with 2.3.2
In order to use CCI classes, a header must be included
As with SystemC, CCI code is defined in a specific namespace
namespace cci;
#include <cci_configuration>

## Slide 6: Configuration Overview
User I/F
Custom Type Support
Packaging
originator
cci_value
cci_value_converter
custom broker
broker
Inter-module configuration
Basic configuration
Response to / Validation of Parameter Value Changes
callbacks
parameter
handle
Configuration Tasks
How common (relatively)
Relevant parts of the standard

## Slide 7: Key Configuration Components
Parameter
  consists primarily of a name (string) and a value
  is an instance of cci_param<T> (T is the value type)
  registers with a broker at construction
  provides 2 interfaces to set/get values
    “untyped”: uses variant type; interoperable with JSON
    “typed”: a templated interface using instantiated type T
Broker
  Manages access to parameters registered with it
    Used by both models and infrastructure/tools
  Two kinds of brokers:
    There is one common global broker
    Any number of custom brokers may also exist

## Slide 8: Key Classes & Interactions
cci_broker_if
cci_param(_untyped)_handle
cci_param
parameter owner
(SystemC module)
parameter user
(SystemC module, tool, etc.)
typed access
untyped access
request parameter
handle
specify preset value (overrides default)
cci_param_typed_handle
registration, initialization
specify default value

## Slide 9: Default and Preset Values
The broker allows a PRESET parameter value to be specified prior to the parameter’s construction:
cci::cci_param<int> my_param("param_name", 42);
cci::cci_get_broker().set_preset_cci_value( "param_name", cci::cci_value(10));
The parameter will use the PRESET value if it exists, otherwise it will use the DEFAULT value.
std::cout << my_param.get_value(); // Output = 10
When you create a parameter, you must specify a DEFAULT value:

## Slide 10: Actual vs. Variant Value Types
There are two ways to access parameter values:
Untyped: using a variant type, cci_value
  Complex types emulated as collection of primitive types
    Built-in support for basic and SystemC type conversions
    Extensible to support user-defined types
  Important for tool enabling, for example:
    Applying preset values from an ASCII configuration file
    Presenting/validating values of complex parameter types
Typed: using the template instantiated value type
  More direct (and efficient) when value type is known
Note: cci_value may be promoted to core language as sc_variant.

## Slide 11: Originator
The origin of a parameter’s current value is always known; the cci_originator class is used for this
Within the SystemC module hierarchy, originator modules are determined automatically
  e.g. “top.platformX.subsystemA.dma1”
Identifying strings are provided outside the SystemC module hierarchy
  e.g. “platformX_basic_configuration.cfg” Indicating the value came from a configuration file
  e.g. “sim_user” Indicating the value was set interactively
Originators are generally managed behind-the-scenes

## Slide 12: Parameter Handles
Returned by a broker for name-based parameter lookup
Provides a parameter-like interface
Informs parameter of originator when value is updated
Available in both untyped and typed forms:
class cci_param_untyped_handle;
template<typename T> class cci_param_typed_handle;

## Slide 13: Parameter and Handle
cci_param_untyped
cci_param_typed
cci_param_untyped_handle
cci_param_typed_handle
cci_param_if
Handles redirect calls to original parameter, passing the originator
For convenience:
typedef cci_param_untyped_handle cci_param_handle
template<typename T> using cci_param = cci_param_typed<T>; (pre-C++11: #define cci_param cci_param_typed)
xxx_param_untyped
xxx_param_typed
Provided by the standard
Custom parameter implementation(s)
Default parameter implementation

## Slide 14: Standard vs Implementation
Standard:
  Parameter and broker interface
  Default implementation of cci_param
  Originator and Handle
  Callback Infrastructure
  cci_value
Vendor Implementation:
  Specialized brokers
  Support for configuration files (xml, conf…)
Note: the POC implementation provides example brokers in cci_utils/

## Slide 15: A parameter owner module
SC_MODULE(simple_ip) {
private:
cci::cci_param<int> int_param;
public:
SC_CTOR(simple_ip) : int_param("int_param", 0)
{
int_param.set_description("...");
SC_THREAD(do_proc);
}
void do_proc() {
for(int i = 0; i < int_param; i++) {
...
}
}
};
Parameters are usually private members forcing brokered access
Default values must be supplied using the constructor argument
Owner reads parameter’s value

## Slide 16: Accessing Parameter Values
When value type is known, call parameter's set_value(T val) or get_value() function
  Common C++ types
  SystemC Data types
  Extensible to user-defined types
When parameter type is unknown or unsupported:
  Use cci_value representation (variant type)
  set_cci_value()
    Takes variant typed value; fails if incompatible contents
  get_cci_value()
    Returns variant typed value

## Slide 17: Broker Lookup of Params (1)
SC_MODULE(configurator) {
cci::cci_broker_handle m_brkr;
SC_CTOR(configurator)
: m_brkr(cci::cci_get_broker())
{
sc_assert(m_brkr.is_valid());
SC_THREAD(do_proc);
}
…
Get handle to broker associated with this module
Declaration of broker handle variable

## Slide 18: Broker Lookup of Params (2)
void do_proc() {
const std::string int_param_name = "top.sim_ip.int_param";
cci::cci_param_handle int_param_handle =
m_brkr.get_param_handle(int_param_name);
if(int_param_handle.is_valid()) {
cci::cci_value value = int_param_handle.get_cci_value();
value = value.get_int() + 1;
...
int_param_handle.set_cci_value(value);
...
}
Get handle to named parameter from broker
Get current parameter value
Set new parameter value
Check handle validity / parameter exists

## Slide 19: Parameter Mutability
Parameters are mutable by default
Mutability is set by template parameter
Parameters may also be made immutable
Locking can be used to make a mutable parameter temporarily immutable
  E.g. to prohibit post-elaboration changes to parameters affecting design structure
cci::cci_param<int, CCI_MUTABLE_PARAM> p1;
cci::cci_param<int, CCI_IMMUTABLE_PARAM> p2;

## Slide 20: Description and Metadata
CCI parameters have a description intended to explain their purpose and usage to a simulation user.
Supplied either as a constructor argument or with a setter.
my_param.set_description("Clock frequency");
my_param.add_metadata("units", "V", "Units of the value");
my_param.get_metadata(); // Return CCI values
CCI parameters have array of meta information (cci_value_map)
Can use this for any purpose

## Slide 21: Brokers
A broker may be registered with global scope or at a specific point in the module hierarchy
  Where no broker is explicitly registered, the parent’s broker is inherited
A broker must be in place prior to constructing parameters
  Parameters are associated with the reigning broker
Module level brokers are undiscoverable outside of their associated module hierarchy (“private” in nature)
  Parameters are therefore inaccessible from outside that hierarchy
Module level brokers facilitate encapsulation of IP configuration
  E.g. a configurator that applies pre-compiled configuration

## Slide 22: Broker Example
SC_CTOR(SubsystemA)
{
cci_register_broker(my_priv_broker);
}
Only module itself can specify its broker
Top
SubsystemA
SubsystemB
IP_W
IP_Q
IP_R
IP_X
parameters managed by my_global_broker (registration not shown)
parameters managed by my_priv_broker

## Slide 23: Callbacks
Used to track parameter value changes: pre-read, post-read, pre-write and post-write
Parameter creation and destruction callbacks are also available through the broker
Callbacks contain a payload and can return a value
Callback payloads can be typed or untyped
Compatible with C++11 lambdas, function objects
Internal callback mechanism provided by the standard
Note: The callback mechanism may be provided more widely across SystemC in the future.

## Slide 24: Parameter Owner Callback
SC_MODULE(simple_ip) {
private:
cci::cci_param<int> P1;
cci::cci_callback_untyped_handle P1_cb;
public:
SC_CTOR(simple_ip): P1("P1", 0) { P1_cb = P1.register_post_write_callback(&simple_ip::cb,this);
...
}
void cb(const cci::cci_param_write_event<int> & ev);
...
Post-write callback registered in constructor
Post-write callback function with the write event as parameter
Callback handle

## Slide 25: Callback Events
Callback pre_write and post_write event:
  Contains an untyped parameter handle, the old value, new value and the originator
Callback pre_read and post_read event:
  Contains an untyped parameter handle, the value and the originator
Callback create_param and destroy_param event:
  Contains the untyped parameter handle
Support for lambdas/function objects/sc_bind allows customization for different signatures and stateful callbacks

## Slide 26: Custom types
Support for legacy parameter implementation is done via the cci_param_if interface
  Explicit registration with the broker is required
cci_value provides an extensible infrastructure to add packing/unpacking support for custom C++ datatypes.
When a custom C++ data type is extended with cci_value support, it can be transparently used with cci_param

## Slide 27: Summary Usage
The typical modeler will use only a limited subset of the standard on a routine basis.
User I/F
Custom Type Support
Packaging
originator
cci_value
cci_value_converter
custom broker
broker
Inter-module configuration
Basic configuration
Response to / Validation of Parameter Value Changes
callbacks
parameter
handle